## Slide 1: Memory Management

## Slide 2: Agenda
Basics: Address space
Virtual memory
Address translation
Segmentation
Paging
Page replacement algorithms
Design of page table
Page faults and thrashing

## Slide 3: Address space
Early computers ran one process at a time
  The process can occupy whole physical memory except a small portion reserved for OS code and data
With multiprogramming, there are two options
  Give whole memory to the currently running process
    Slow because we need to swap in the code and data of a scheduled process and swap out the code and data of a decheduled process
  Leave the memory-resident code and data of the processes in memory as long as possible
    Fast because need to save/restore only registers on context switch
    How to assign addresses to processes?
    What if memory is full? What about protection/isolation?

## Slide 4: Address space
Each process is assigned a distinct address space
  Each address space starts at address zero and goes up to 2v-1 where v is the width of virtual address
  All addresses in an address space are virtual addresses
  A program can generate only virtual addresses
  In some OS, each address space is assigned a distinct ID, referred to as ASID
    Each ASID has a one-to-one correspondence with PID
    A process can have only one ASID
  Address space of a process contains code (set of instructions), global static data, dynamic data (heap), and stack

## Slide 5: Address space: An example
Stack
Heap
Static/Global
Code/Text
Reserved
Virtual addresses
0
0x004000000
0x10000000
0x10010000
Initial sp = 0x7ffffffc
Reserved

## Slide 6: Address space
Each process is assigned a distinct address space
  The job of the OS is to map demanded portions of the address space of a process to free blobs of physical memory and maintain this mapping
    Virtual to physical address mapping
    All memory accesses go through a virtual to physical address translation
Address space abstraction is needed for isolation
  The job of the OS is to keep the code/data of a process isolated from other processes
    Address space abstraction helps achieve this through address mapping
  Central component of memory virtualization

## Slide 7: Basics of memory management
Basic requirement of memory management is two-fold: correctness and security
  A process should read from or write to a piece of data if and only if the piece of data belongs to that process
Memory management is done at two levels
  By OS and by each process
    OS manages the physical memory
    Each process manages its own virtual memory with the help of OS

## Slide 8: Process-level memory management
Stack memory is managed automatically by compiled code
  Compiler generates fills from and spills to stack
Two operations for managing process heap: allocation and de-allocation
  Allocations done through standard library functions such as malloc, calloc, realloc, etc. in C
  Deallocation done through library function free
  Different languages have different functions
Allocation function invokes the brk or sbrk system call if needed

## Slide 9: Process-level memory management
Allocation functions invoke sbrk or brk system call only if needed
  If the heap allocated so far needs to be extended, the system call is invoked to extend the “memory break” of the process
Deallocation functions just return the freed memory to the heap of the process
All allocated memory of a process is reclaimed by OS when the process exits
  Therefore, not freeing memory for a short-lived process does not lead to any problem
Not freeing memory that is no longer used by long-running processes leads to memory leak

## Slide 10: Process-level memory management
A process can also use mmap() to dynamically allocate memory
  A wrapper around the mmap system call
  mmap allocates memory in two possible ways
    Maps a file (or a portion thereof) to memory and uses the file space to back up this memory space
    Allocates memory backed by swap space (which doesn’t belong to any file); this is referred to as anonymous mapping
  mmap allows sharing the allocated memory across processes without requiring shmget/shmat calls

## Slide 11: Physical address binding
  Every piece of data has an address and the address can be determined at three different points: compilation, loading, and execution
If the compiler knows exactly where a data will be placed in memory, it can generate absolute addresses
  Reduces flexibility in memory allocation
  How to bind addresses for dynamically allocated data?
  How to handle a process, size of which exceeds the size of the available memory?
  How to handle multiple processes?

## Slide 12: Physical address binding
Usually, the compiler generates relative addresses
  All the addresses are relative to some address such as stack pointer, global pointer, etc.
  Loader carries out the absolute address binding
  Lots of flexibility in memory allocation, but needs an additional level of translation at run-time
  How to handle a process, size of which exceeds the available memory size?
Ideally, we want to load parts of the process as and when needed and do physical address binding at that time

## Slide 13: Virtual memory
With a 32-bit address, one can access 4 GB of memory
  A process will never get the complete memory though
  Seems enough for most day-to-day applications
  However, it seems unfair to load the entire application executable at startup
    A process will never require the complete executable at any point in time
    Takes away memory from other processes and hurts the degree of multiprogramming
  Virtual memory offers an address space and a translation mechanism in computer systems that help decouple the logical and physical views of memory

## Slide 14: Virtual memory
Virtual or logical memory consists of the address space that every process sees
  This is the process’s view of the memory and every process sees exactly the same address space
  The size of this address space is determined by the instruction set architecture of the processor
    Datapath width
  In a 32-bit architecture, every process gets 4 GB virtual address space
    Some of it is usually reserved for kernel use and the rest is given to the process
    Text, global constants, heap, and stack reside in the virtual address space and get mapped dynamically to physical memory by the OS through address translation

## Slide 15: Address translation
Act of translating virtual addresses to physical addresses at run time
  Each memory access requires this translation
  Done in hardware for speed
  Can be done using just two new hardware registers base address and bound, provided the address space of a process is mapped contiguously to physical memory
    Just add the base register contents to virtual address to get the physical address; check that the generated physical address is within the bound
    On a context switch, save and restore these two registers
    Need kernel mode instructions to write to these registers

## Slide 16: Address translation
Act of translating virtual addresses to physical addresses at run time
  Can be done using just two new hardware registers base address and bound, provided the address space of a process is mapped contiguously to physical memory
  Unfortunately, mapping the address space of a process contiguously to physical memory poses significant challenges
    What if there is no big enough free hole in physical memory?
    What if the process needs to grow at run time?
    Seems wasteful to reserve full address space at start of a process (the space between stack and heap is wasted)

## Slide 17: Segmentation
Wasted memory can be reduced by having a (base, bound) pair for each segment
  One pair each for code, global, heap, and stack segments
  OS can place a segment in any free hole of physical memory that is large enough to accommodate the segment
    Needs to maintain a list of free physical memory holes
    What if a segment grows too much to fill up the allocated hole or what if there isn’t a big enough hole to begin with?
    Still, there is wasted holes of small sizes: external fragmentation
  Any access outside the bound of a segment leads to a segmentation fault; also needs rwx permission check
  Segments can be identified by upper few bits of virtual address (e.g., 00, 01, 10, 11 for CS, GS, HS, SS)

## Slide 18: Paging
Segmentation requires the OS to be able to accommodate variable-sized segments some which can also grow
This drawback is addressed by paged virtual memory
  The process address space is divided into equally sized small units called pages
  To get rid of external fragmentation, the physical memory is also divided into equal-sized units called page frames
  A virtual page is loaded into a page frame selected at run-time only when the virtual page is needed
    This is called demand paging (only internal fragmentation)
  The CPU generates virtual addresses while executing
  Even though the virtual pages of a process are contiguous, physical pages need not be
    A virtual to physical page number translation is needed

## Slide 19: Paging
Example
  int *a = (int*)malloc(8000*sizeof(int));
  for (int i=0; i<8000; i++) a[i] = 0;
  Virtual memory for array “a” is allocated by malloc
    Virtual memory allocated = 32000 bytes (sizeof(int) is 4)
    No physical memory is allocated yet
  Assume the page size to be 4096 bytes
    One page can hold 1024 contiguous elements of “a”
    Assume that “a” occupies virtual pages 10 to 17
  When a[0] is accessed in the first iteration of the loop, the first virtual page of “a” is accessed from physical memory, but the physical page is not there
    OS allocates one free physical page frame (say PF#3) and remembers the mapping VPN 10  PFN 3 in the page table of the process (each process has a page table)

## Slide 20: Paging
Example (continued)
  int *a = (int*)malloc(8000*sizeof(int));
  for (int i=0; i<8000; i++) a[i] = 0;
  Second page of “a” gets accessed when loop reaches i=1024
    OS allocates another free page frame (say, PF#7) and adds a new mapping VPN 11  PFN 7 to the page table of the process
  Next page frame gets allocated when i=2048 and so on
  The allocated 8 page frames remain in memory until the OS is forced to swap out some of the pages due to shortage of physical memory

## Slide 21: Paging
Virtual to physical address translation
  Every virtual address is divided into two parts: virtual page number and page offset
  The page offset remains unchanged in the translation
  The virtual page number is translated to a physical page frame number
  The translation is maintained in a per-process page table
  The first step in this translation is to access the page table (for now, let’s assume a contiguous page table)
    Every process has a page table base register (PTBR) loaded by the loader; it is a part of the process context and stores the starting physical address of the page table
    Necessary offsets are added to the PTBR

## Slide 22: Paging
Page table entry and page faults
  A page table entry (PTE) contains several pieces of information
    A valid bit, present bit, a dirty bit, permission bits (rwx), a mode bit, a reference or accessed bit, and the much needed translation
    The present bit indicates if the page is currently present in physical memory and if not, the result is a page fault
    The valid bit indicates whether the page has a valid PTE
  A page fault is handled by raising a restartable exception (which generates a trap) and the page fault handler of the OS handles the exception in software
    After handling the exception, the process undergoing the page fault returns from trap and restarts from the same instruction that suffered from a page fault (contrast syscall)

## Slide 23: Paging
Page fault handling
  Save context (same as done in any trap e.g., syscall)
  Locate the needed page in the next level of storage
  Find or create a free physical page frame to accommodate the newly brought in page
  Start a copy operation via DMA and invoke the process scheduler to pick a new process to run
  On DMA completion, make appropriate changes in the page table
  Start a DMA operation to write the replaced page to the next level of storage, if the dirty bit is set

## Slide 24: Paging
Page fault handling
  Since the next level of storage is disk, the swap-in and swap-out operations are slow
  A part of the disk is maintained as a swap partition
    This partition is maintained using lower-overhead techniques so that reading from and writing to this partition is fast
  A page replaced from memory is kept in the swap partition until it has to be evicted (due to finite swap space) and moved to its original location in the file system (anonymous pages stay in swap partition)
    The swap partition is a fast victim cache for the memory
    The page replacement algorithm plays an important role; its goal is to minimize the number of page faults

## Slide 25: Paging
Who does page replacement and when?
  Page replacement is done ahead of time by the swap daemon or a page daemon
    A process that runs only in kernel mode
  The page daemon usually sleeps and it is woken up only when the number of free pages reaches a certain threshold
    This threshold is usually referred to as the low watermark
  The page daemon selects pages to replace and continues running until the number of free pages reaches another threshold referred to as the high watermark
    Number of free pages is kept between HWM and LWM

## Slide 26: Paging
Virtual to physical address translation
  Once the physical page frame number is available, it is appended in front of the page offset to get the physical address, which can now be used to access the data item
  Two memory accesses to get a data item: one to get the translation and another to get the data
  Translation-related memory accesses can be reduced in number by caching a subset of the translations used recently inside the processor
    This cache is called translation look-aside buffer (TLB), one for instruction and one for data
    A TLB entry contains a tag (derived from the virtual page number), a PTE, an address space id, a valid bit, repl. bits
    A TLB miss leads to a page table access

## Slide 27: Paging
TLB example
  for (i=0; i<8000; i++) a[i] = 0;
  Assume that each array element is four bytes
  Assume that page size is 4096 bytes
  How many TLB misses if TLB has 16 entries?
How is a TLB miss handled?
  In hardware or by software-based TLB miss exception handler (the latter case goes through a trap)
  After the miss is handled, the instruction is re-executed
What if the TLB is full and there is a new miss?
  Need to replace an entry to accommodate a new one
  Like cache replacement policies: LRU, random, etc.

## Slide 28: Paging
Demand paging poses a performance problem with fork()
  Before starting the child, all pages of the parent need to copied into child’s physical page frames leading to a large number of page faults
  Usually, a copy-on-write policy is followed
    Unless the child or the parent writes to a page after fork(), it is not copied
  This read-only pages are shared between parent and child
  On a fork() call, the parent’s page table is copied into the child’s; in both page tables the data pages are set to read-only permission and code pages are set to execute-only permission

## Slide 29: Page replacement algorithms
A page replacement algorithm is an online algorithm
  Takes a sequence of accesses in the form (VA, pid) and returns (fault, PPFN) or (no fault, PPFN)
    Invoked on all accesses, but replaces a page only on a page fault provided all physical page frames are occupied; otherwise there is no need for page replacement
    In the case of a replacement, selects one of the physical page frames and assigns it to the current access (VA, pid) that has suffered from a page fault
    The goal of a page replacement algorithm is to minimize the number of page faults
    The biggest challenge in these algorithms is that the full input sequence is not known at any point in time as the future accesses are unknown

## Slide 30: Page replacement algorithms
We will transform the input sequence before applying the algorithm
  The actual virtual addresses will be transformed to the corresponding virtual page numbers and the sequence of virtual page numbers forms the input to the algorithm
    Consider a page size of 100 bytes and the virtual address sequence (100, 432, 101, 612, 102, 103, 104, 101, 611, 102, 103, 104, 101, 610, 102, 103, 104, 101, 609, 102, 105), which will be transformed to (1, 4, 1, 6, 1, 1, 1, 1, 6, 1, 1, 1, 1, 6, 1, 1, 1, 1, 6, 1, 1) and we will deal with this transformed sequence only

## Slide 31: Page replacement algorithms
The most popular deterministic replacement algorithms include FIFO, LRU, LFU, and a large number of approximations of LRU
  The FIFO policy replaces the oldest page provided all physical page frames are occupied
    Consider a memory with three physical page frames and the access sequence (7, 0, 1, 2, 0, 3, 0, 4, 2, 3, 0, 3, 2, 1, 2, 0, 1, 7, 0, 1); this sequence experiences fifteen page faults with FIFO replacement
    It may not be always true that having more page frames reduces the number of page faults with FIFO replacement
    Consider the sequence (1, 2, 3, 4, 1, 2, 5, 1, 2, 3, 4, 5) and compare the number of faults with three and four page frames when using FIFO replacement

## Slide 32: Page replacement algorithms
The LRU replacement algorithm replaces the least recently used page
  Needs to maintain the order of accesses to the pages
  Every page access needs to update this order
  The sequence on which FIFO has fifteen page faults, LRU has twelve page faults
  The motivation for LRU policy comes from the optimal algorithm
    An algorithm that replaces the page with the furthest access in the future is provably optimal (due to Laszlo Belady, 1966); also known as the longest forward distance (LFD) replacement algorithm
    This algorithm cannot be implemented due to dependence on future
    LRU is a crude approximation of the optimal algorithm

## Slide 33: Implementing LRU
Two ways of implementing LRU: counter-based and list-based (usually known as stack-based)
  A counter-based implementation attaches a time-of-access field with each page frame
    On each access, this field is updated with the current hardware clock tick; the page with the smallest tick is replaced
    Three drawbacks: the size of this field must be equal to the size of the hardware clock register, handling wrap-around is difficult, replacement requires a find-min operation
  Possible to maintain relative time instead of absolute time
    On an access to a page frame, its time field is reset to zero and all others’ time fields are incremented by one; the page with the largest count is replaced

## Slide 34: Implementing LRU
List-based implementation
  Maintains a doubly-linked list of page frame ids
  The head of the list is the MRU frame and the tail is the LRU frame
  On each access, the accessed frame is delinked and made the head of the list
    Requires O(1) pointer operations
  Does not suffer from the drawbacks of the counter-based implementations
  Still requires O(nlog n) space to store the recency list for n physical page frames
  In reality, some approximation of LRU is implemented that needs only O(n) space
    Let us discuss such approximate schemes

## Slide 35: Reference bit algorithm
For each page frame, there is a reference bit and a k-bit register
  k is usually a small constant
  The reference bit is set on each access to the frame
  Periodically, all the registers are shifted to right by one bit and the reference bits are copied to the most significant position of the register; at this time all the reference bits are cleared
  The page frame with the smallest register value is replaced; requires a find-min operation, which is O(n)
  The register value of a frame is the history of accesses to the page frame during the last k periods

## Slide 36: Second chance algorithm
We have just the reference bit per page frame
The idea is to replace the page in the FIFO order that has its reference bit reset
  If at the time of replacement, the oldest page has its reference bit set, it is skipped but its reference bit is reset i.e., it is given a second chance to get accessed
  LRU-CLOCK is one of the simplest implementations
    The page frames are organized in a circular FIFO queue with a pointer pointing to the next replacement candidate (this is like a clock hand)
    If the replacement candidate has its reference bit set, the reference bit is reset, the pointer is moved to the next entry, and the process continues until a replacement candidate is found; its reference bit is set and the pointer is moved to the next frame

## Slide 37: Design of page table
Organization of page table
  The page table access algorithm implicitly assumes that the page table is stored in a contiguous portion of physical memory
    Let’s see if it is practical by computing how large the page table is
    Notice that all translations resident in the page table are not needed simultaneously with high probability
    Assume that the page size is 2p bytes, the virtual address space is 2v bytes, and the PTE size is 2t bytes; this leads to a page table size of 2v-p+t bytes which is 8 MB for v=32, p=12, and t=3; this is just for one process
  To conserve memory, page tables are also paged just like the processes
    Called hierarchical paging and affects how a PTE is located

## Slide 38: Design of page table
Reserving a large contiguous memory space for a linear page table is wasteful
  The program doesn’t need the entire page table at any point in time; many page table entries may not be needed while running
Larger page size reduces page table size, but increases internal fragmentation
Can use segmentation and paging together to reduce the page table size
  Maintain one linear page table per segment
    Base and bound registers of a segment maintain the starting address and size of that segment’s page table

## Slide 39: Design of page table
Paged segments avoid allocating page table entries for unused parts of a segment
  External fragmentation in allocation of page table
  Growing segments may need page tables to grow
Popular solution: page the page table
  Avoids allocating pages of the page table (PT) that have only invalid PTEs; reduces PT size significantly
  Need a “page directory table” to locate pages of PT
  The page directory table is large, so that is also paged
  General principle: any level of page table that is larger than a page is paged to avoid reserving contiguous memory larger than a page

## Slide 40: VA to PA translation: An example
9 bits
9 bits
9 bits
9 bits
12 bits
VA
PTBR
+
<<3
64 bits
L4 table
+
<<3
L3 table’s one page
64 bits
<<3
+
64 bits
L2 table’s one page
<<3
+
64 bits
L1 table’s one page
PTE
TLB misses are very expensive: four memory accesses
Two levels of TLB with very large L2 TLB
Small page structure caches (PSCs) or page walk caches (PWCs) to cache recently used L4, L3, L2 table’s entries

## Slide 41: VA to PA translation: An example
Step#1: Look up L1 TLB; on a hit, return PTE
Step#2: Look up L2 TLB; on a hit, insert PTE in L1 TLB and return PTE
Step#3: Invoke hardware page walker to handle TLB miss (some processors use software TLB miss handlers, but with multi-level page table, that is slow)
  Step#3A: Look up the PSCs in parallel and retrieve entries that are not found in the PSCs one at a time from physical memory; continue until PTE is obtained; insert each level entry in PSCs
  Step#3B: insert PTE in both L1 and L2 TLBs

## Slide 42: Page faults and thrashing
A process uses a set of pages quite frequently before moving on to another set of pages
  The set of pages accessed over a time window (representing a locale of the program) is called the working set of the process
    The working set keeps changing with time
  A process is said to be thrashing if it is suffering from an excessive volume of page faults
    Happens if the process fails to get enough page frames to accommodate its working set

## Slide 43: Page faults and thrashing
Pre-paging
  When a new process is swapped in, thrashing may occur until the process has its working set in the memory (lot of page faults in the beginning)
    Pre-paging or prefetching is used to solve this problem
  The last seen working set of a process is stored along with its context and the OS swaps in these pages before scheduling the process
    This is called pre-paging or prefetching
    Downside: The working set may not be accurate and some of the swapped in pages may not be used
  Thrashing can also be controlled by increasing or decreasing the degree of multi-programming depending on the page fault count
    Referred to as admission control algorithm