## Slide 1: Computer Networks I Error Correction
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Error Correction
Backward error correction: Correction of detected errors usually requires data blocks to be retransmitted
Not appropriate for some wireless applications:
  The bit error rate (BER) on a wireless link can be quite high, which would result in a large number of retransmissions
  Propagation delay is very long compared to the transmission time of a single frame

## Slide 3: Error Correction
Forward error correction: Need to correct errors on basis of bits received

## Slide 4: Error Correction
Hamming distance:
  d(v1, v2) – Hamming distance in between any two binary sequences v1 and v2
    d(v1, v2) is the number of bits in which v1 and v2 disagree

## Slide 5: Error Correction
Codeword of bits = message bits +check bits
Valid/legal and invalid/illegal codeword:
  Total possible codewords with bits is
  All data messages are legal  each one of them has 1 legal codeword
  All remaining codewords are invalid
0000000000
0000011111
1111100000
1111111111

## Slide 6: Error Correction
Given an algorithm for calculating the check bits
  We can construct the list of valid codewords
Hamming distance of the code: Smallest Hamming distance in between any two valid codewords
0000000000
0000011111
1111100000
1111111111

## Slide 7: Error Correction
To detect bit errors, we need a distance code
  With such a code, there is no way that a single bit error can change a valid codeword to another valid codeword

## Slide 8: Error Correction
To correct bit errors, we need a distance code
  With such a code, the legal codewords are so far apart that even changes, the original codeword is still closer, than any other codeword

## Slide 9: Error Correction
To correct bit errors, we need a distance code
  Original codeword can be uniquely detected based on the assumption that a larger number of errors are less likely  time consuming search

## Slide 10: Error Correction
Codeword of bits = message bits +check bits
We want to design a code that allows all single bit error to be corrected
  Each of the legal messages  there is n illegal codewords at a distance 1 from it
  As there are total number of bit patterns

## Slide 11: Error Correction
Codeword of bits = message bits +check bits
We want to design a code that allows all single bit error to be corrected
  Each of the legal messages  there is n illegal codewords at a distance 1 from it
  As there are total number of bit patterns
  So, given , this put a lower bound on the check bits that are needed to correct single bit errors
    For = 4, = 3
    For = 7, = 4

## Slide 12: Hamming Code
M7
M6
M5
P4
M3
P2
P1

## Slide 13: Hamming Code
M7
M6
M5
P4
M3
P2
P1

## Slide 14: Error Correction Codes
Convolution codes: GSM mobile phone system, satellite communications, 802.11
Reed-Solomon code: DSL, data over cable, satellite communications, CDs
Low-density parity check: Digital video broadcasting, Ethernet, 802.11

## Slide 15: Summary
Different error correction techniques discussed:
  Backward error correction
  Forward error correction
  Hamming distance
  Hamming code