## Slide 1: Computer Networks I Data Link Control Protocols (Medium Access Control Protocols) (Channel Partitioning, Taking Turns)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Multiple access links, protocols
Two types of “links”:
Point-to-point
  Point-to-point link between Ethernet switch, host
Broadcast (shared wire or medium)
  Old-school Ethernet
  802.11 wireless LAN, 4G/5G, satellite
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: WiFi
shared wire (e.g.,
cabled Ethernet)
shared radio: 4G/5G

## Slide 3: Multiple access protocols
Single shared broadcast channel
Two or more simultaneous transmissions by nodes:
  Collision if node receives two or more signals at the same time
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Multiple access protocol

## Slide 4: An ideal multiple access protocol
Given: multiple access channel (MAC) of rate R bps
Desired rate:
  1. When one node wants to transmit, it can send at rate R
  2. When M nodes want to transmit, each can send at average rate R/M
  3. Fully decentralized:
    No special node to coordinate transmissions
    No synchronization of clocks, slots
  4. Simple

## Slide 5: MAC protocols: taxonomy
Three broad classes:
Channel partitioning
  Divide channel into smaller “pieces” (time slots, frequency, code)
  Allocate piece to node for exclusive use
Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns
Random access
  Use randomization for handling collisions
  “Recover” from collisions

## Slide 6: Channel partitioning protocols: TDMA
TDMA: Time division multiple access
Access to channel in “rounds”
Each station gets fixed length slot (length = packet transmission time) in each round
Unused slots go idle
Example: 6-station scenario, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 7: Channel partitioning protocols: FDMA
FDMA: Frequency division multiple access
Channel spectrum divided into frequency bands
Each station assigned fixed frequency band
Unused transmission time in frequency bands go idle
Example: 6-station scenario, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 8: MAC protocols: taxonomy
Three broad classes:
Channel partitioning
  Divide channel into smaller “pieces” (time slots, frequency, code)
  Allocate piece to node for exclusive use
Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns
Random access
  Use randomization for handling collisions
  “Recover” from collisions

## Slide 9: “Taking turns” MAC protocols
Polling:
Centralized controller “invites” other nodes to transmit in turn
Typically used with “dumb” devices
Concerns:
  Polling overhead
  Latency
  Single point of failure (master)
Bluetooth uses polling
centralized controller
client devices
poll
data
data

## Slide 10: “Taking turns” MAC protocols
Token passing:
Control token message explicitly passed from one node to next, sequentially
  Transmit while holding token
Concerns:
  Token overhead
  Latency
  Single point of failure (token)
T
data
(nothing
to send)
T

## Slide 11: Summary
Multiple Access Control:
  Channel partitioning, by time, frequency or code
    TDMA, FDMA
  Taking turns
    Polling from central site, token passing