## Slide 1: Computer Networks Data Link Control Protocols (Medium Access Control Protocols) (Random Access Protocols: ALOHA)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: MAC protocols: taxonomy
Three broad classes:
Channel partitioning
  Divide channel into smaller “pieces” (time slots, frequency, code)
  Allocate piece to node for exclusive use
Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns
Random access
  Use randomization for handling collisions
  “Recover” from collisions

## Slide 3: Random access protocols
When node has packet to send
  Transmit at full channel data rate R
  No a priori coordination among nodes
Two or more transmitting nodes: “collision”
Random access protocol specifies:
  How to detect collisions
  How to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 4: Slotted ALOHA
Assumptions:
All frames same size
Time divided into equal size slots (time to transmit 1 frame)
Nodes start to transmit only slot beginning
Nodes are synchronized
If 2 or more nodes transmit in slot, all nodes detect collision
Operation:
When node obtains fresh frame, transmits in next slot
  If no collision: node can send new frame in next slot
  If collision: node retransmits frame in each subsequent slot with probability p until success

## Slide 5: Slotted ALOHA
Pros:
Single active node can continuously transmit at full rate of channel
Highly decentralized: only slots in nodes need to be in sync
Simple
Cons:
Collisions, wasting slots
Idle slots
Clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C: Collision
S: Success
E: Empty

## Slide 6: Slotted ALOHA: efficiency
Efficiency: Long-run fraction of successful slots (many nodes, all with many frames to send)
Suppose: N nodes with many frames to send, each transmits in slot with probability p
  Prob that given node has success in a slot = p(1-p)N-1
  Prob that any node has a success = Np(1-p)N-1

## Slide 7: Slotted ALOHA: efficiency
Max efficiency: find p* that maximizes Np(1-p)N-1
  Max efficiency = 1/e = .37
At best: channel used for useful transmissions 37% of time!

## Slide 8: Pure ALOHA
Unslotted Aloha: simpler, no synchronization
  When frame first arrives: transmit immediately
Collision probability increases with no synchronization:
  Frame sent at t0 collides with other frames sent in [t0-1,t0+1]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame

## Slide 9: Pure ALOHA efficiency
P(success by given node) = P(node transmits)
×P(no other node transmits in [t0-1,t0]
×P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
  Prob that any node has a success = Np(1-p)2(N-1)
*

## Slide 10: Pure ALOHA efficiency
Max efficiency: find p* that maximizes Np(1-p)2(N-1)
  Max efficiency = 1/2e = .18
Performs even worse than slotted Aloha!

## Slide 11: Pure ALOHA vs Slotted ALOHA
Offered traffic per slot
Efficiency

## Slide 12: Summary
Multiple Access Control:
  Random access MAC protocols
    Slotted ALOHA, Pure ALOHA