## Slide 1: Computer Networks Data Link Control Protocols (Multiple Access Control Protocols) (Random Access Protocols: CSMA)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: MAC protocols: taxonomy
Three broad classes:
Channel partitioning
  Divide channel into smaller “pieces” (time slots, frequency, code)
  Allocate piece to node for exclusive use
Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns
Random access
  Use randomization for handling collisions
  “Recover” from collisions

## Slide 3: Pure ALOHA vs Slotted ALOHA
Offered traffic per slot
Efficiency

## Slide 4: CSMA (carrier sense multiple access)
Simple CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
humans at a cocktail party
(shared air, acoustical)

## Slide 5: CSMA (carrier sense multiple access)
1-persistent CSMA:
  If channel sensed idle: transmit with probability 1
  If channel sensed busy: continuously sense  transmit immediately when channel becomes idle
  If collision: wait for a random time, then start sensing
Nonpersistent CSMA:
    If channel sensed busy: do no sense continuously  wait for a random amount of time and then sense again
    Better channel utilization  longer delay than 1-persistant CSMA
p-persistent CSMA:
  If channel sensed idle: transmit with probability p

## Slide 6: CSMA (carrier sense multiple access)
Offered traffic per slot
Efficiency

## Slide 7: CSMA: collisions
Collisions can still occur with carrier sensing:
  Propagation delay means two nodes may not hear each other’s just-started transmission
  Distance & propagation delay play role in in determining collision probability
Collision: entire packet transmission time wasted
spatial layout of nodes

## Slide 8: CSMA (carrier sense multiple access)
Simple CSMA: listen before transmit:
  If channel sensed idle: transmit entire frame
  If channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  Collisions detected within short time
  Colliding transmissions aborted, reducing channel wastage
  Collision detection easy in wired, difficult with wireless
Human analogy: the polite conversation

## Slide 9: CSMA/CD
CSMA/CD reduces the amount of time wasted in collisions
  Transmission aborted on collision detection
spatial layout of nodes

## Slide 10: Ethernet CSMA/CD algorithm
Ethernet receives datagram from network layer, creates frame
If Ethernet senses channel:
  If idle: start frame transmission.
  If busy: wait until channel idle, then transmit
If entire frame transmitted without collision - done!
If another transmission detected while sending: abort, send jam signal
After aborting, enter binary (exponential) backoff:
  After m-th collision, chooses K at random from {0,1,2, …, 2m-1}
  Wait for K slots, return step 2
  More collisions: longer backoff interval

## Slide 11: Ethernet: unreliable, connectionless
Connectionless: No handshaking between sending and receiving NICs
Unreliable: Receiving NIC doesn’t send ACKs or NAKs to sending NIC
  Data in dropped frames may be recovered by the higher layer protocols (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: 1-persistant CSMA/CD with binary backoff

## Slide 12: Wireless ≠CSMA/CD
Transmitter cannot send/listen concurrently

## Slide 13: Wireless ≠CSMA/CD
Nodes have different coverage areas
  Hidden terminal problem and Exposed terminal problem

## Slide 14: CSMA/CA: MACA  IEEE 802.11
MACA: Sender and receiver uses a short handshake before transmitting
  IEEE 802.11 uses a refinement of MACA
802.11: CSMA - sense before transmitting
802.11: no collision detection!
  Goal: avoid collisions: CSMA/CollisionAvoidance
  Hidden and exposed station problems are alleviated using RTS/CTS exchanges
  In 802.11 RTS/CTS is optional

## Slide 15: CSMA/CA: IEEE 802.11
802.11 sender
1. If sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
If frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2. If sense channel busy then
  start random backoff time in range (0, w-1), w = CWmin
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval (double w upto CWmax), repeat 2

## Slide 16: CSMA/CA: IEEE 802.11
B
A
RTS
CTS
C
D
Silenced

## Slide 17: CSMA/CA: IEEE 802.11
B
A
DATA
ACK
C
D
Silenced

## Slide 18: CSMA/CA: IEEE 802.11
B
A
RTS
CTS
C
D
Not silenced

## Slide 19
Sender first transmits small request-to-send (RTS) packet to the receiver
Receiver replies with clear-to-send CTS in response to RTS
Sender transmits data frame
Nodes receiving CTS defer transmissions
Nodes receiving RTS  defer one CTS time
Nodes receiving RTS but not CTS, free to send
  RTS/CTS may still collide, but less likely (as they’re short)
    RTS/CTS exchange does not entirely solve the hidden and exposed station problem
CSMA/CA: IEEE 802.11

## Slide 20: CSMA/CA: IEEE 802.11
Src:https://www.researchgate.net/publication/26429569_Autonomous_Power_Control_MAC_Protocol_for_Mobile_Ad_Hoc_Networks/figures?lo=1

## Slide 21: IEEE 802.11 Wireless LAN
Src: https://networkustad.com/2019/11/16/ieee-802-11-standards/

## Slide 22: MAC protocols: Comparison
Three broad classes:
Channel partitioning
  Share channel efficiently and fairly at high load
  Inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Taking turns
  Look for best of both worlds
  Single point of failure
Random access
  Efficient at low load: single node can fully utilize channel
  High load: collision overhead

## Slide 23: Summary
Random access based MAC protocols:
  CSMA
  CSMA/CD
  CSMA/CA
Comparison of the MAC protocols