## Slide 1: Computer Networks Local Area Networks
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: MAC Address and Framing

## Slide 3: MAC addresses
MAC (or LAN or physical) address:
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  Each interface on LAN has an unique MAC address
  e.g.: 1A-2F-BB-76-09-AD
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)

## Slide 4: MAC addresses
MAC address allocation administered by IEEE
Manufacturer buys portion of MAC address space (to assure uniqueness)
MAC address: portability
  Can move interface from one LAN to another

## Slide 5: Ethernet frame structure
Sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
Preamble:
Used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011

## Slide 6: Ethernet frame structure
dest.
address
source
address
data (payload)
CRC
preamble
type
Addresses: 6 byte source, destination MAC addresses
  If adapter receives frame with matching destination address, or with broadcast address, it passes data in frame to network layer protocol
  Otherwise, adapter discards frame
Type: indicates higher layer protocol
  Mostly IP but others possible, e.g., Novell IPX, AppleTalk
  Used to demultiplex up at receiver
CRC: Cyclic redundancy check at receiver
  Error detected: frame is dropped

## Slide 7: 802.11 frame structure

## Slide 8: Ethernet Switches

## Slide 9: Ethernet: physical topology
Bus: popular through mid 90s
  All nodes in same collision domain (can collide with each other)
Bus
Switched
Switched: prevails today
  Active link-layer 2 switch in center
  Each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 10: Ethernet switch
Switch is a link-layer device
  Store, forward Ethernet frames
  Examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent: hosts unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured

## Slide 11: Ethernet switch
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  No collisions; full duplex
  Each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
https://www.ciscopress.com/articles/article.asp?p=2111396

## Slide 12: Ethernet switch
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  No collisions; full duplex
  Each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  But A-to-A’ and C to A’ can not happen simultaneously

## Slide 13: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: How does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: Each switch has a forwarding table, each entry:
  (MAC address of host, interface to reach host, time stamp)
Q: How are entries created, maintained in forwarding table?

## Slide 14: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
Switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Forwarding table
(initially empty)
A
1
60
  When frame received, switch “learns” location of sender: incoming LAN segment
  Records sender/location pair in switch table

## Slide 15: Self-learning and Forwarding
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
Frame destination, A’, location unknown: flood
Destination A location known:
selectively send
on just one link

## Slide 16: Interconnecting switches
Self-learning switches can be connected together:
Q: Sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: Self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 17: Switch: frame filtering/forwarding
When frame received at switch:
  1. Record incoming link, MAC address of sending host
  2. Index forwarding table using MAC destination address
  3. If entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 18: Virtual LAN

## Slide 19: Virtual LANs (VLANs)
Administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
Single broadcast domain:
  Scaling: all layer-2 broadcast traffic (i.e. unknown MAC) must cross entire LAN
  Efficiency, security, privacy issues

## Slide 20: Port-based VLANs
1
8
2
7
9
16
10
15
Switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure
Virtual Local Area Network (VLAN)
Port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 21: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
Traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
Dynamic membership: ports can be dynamically assigned among VLANs
Forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 22: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
Trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches must carry VLAN ID info
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 23: Summary
Local area networks:
  MAC addresses and framing
  Ethernet switch and self learning
  Virtual LANs