## Slide 1: Computer Networks Hubs and Switches
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Hubs vs Switches
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 3: Hubs vs Switches

## Slide 4: Hubs
Bits coming from one link is repeated to all other links
No frame buffering
No CSMA/CD at hub
  One large collision domain
Hub: A-to-A’ and B-to-B’ cannot transmit simultaneously
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 5: Switches
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  No collisions; full duplex
  Each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
Hubs vs switch: https://community.fs.com/blog/do-you-know-the-differences-between-hubs-switches-and-routers.html

## Slide 6: Cut-through Switches
Switches start forwarding the frames just after reading the destination address
  Slightly reduces the latency
A
A’
B
B’
C
C’
1
2
3
4
5
6
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 7: Switches vs. routers
Both are store-&-forward:
Routers: network-layer devices (examine network-layer headers)
Switches: link-layer devices (examine link-layer headers)
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 8: Switches vs. routers
Both have forwarding tables:
Routers: compute tables using routing algorithms, IP addresses
Switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 9: Hubs vs Switches vs Routers

## Slide 10: Summary
Hubs and switches:
  Hubs
  Switches
    Cut-through switches
  Routers