## Slide 1: Computer Networks II IP Forwarding and Address Allocation
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: IP forwarding

## Slide 3: Package Forwarding in a Postal System
Destination prefix | Next hop
UP | Lucknow flight
West Bengal | Kolkata flight
Maharashtra | Mumbai flight
Postal analogy:
6 packages need to be sent in these addresses
UP, Prayagraj, Barrister Mullah Colony, Swati
UP, Kanpur, Kalyanpur, Amit
West Bengal, Kharagpur, Inda, Manoj
West Bengal, Durgapur, Mahatma Gandhi Rd, Prakash
Maharashtra, Pune, Shivaji Nagar, Vivek
Maharashtra, Nasik, Old Agra Road, Anand
Src: https://pxhere.com/en/photo/1625663

## Slide 4: IP Forwarding
IP addresses on a network belongs to the same prefix
Nodes use a forwarding table that lists the prefixes and the corresponding next hop/link interface
  Improves scalability  reduces the forwarding table size
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24
Prefix | Next hop/interface
223.1.1.0/24 | 223.1.1.4
223.1.2.0/24 | 223.1.2.9
223.1.3.0/24 | 223.1.3.27

## Slide 5: IP Forwarding
But what happens if ranges don’t divide up so nicely?
3
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 6: Longest Prefix Matching
When looking for forwarding table entry for given destination address, use longest address prefix (most specific entry) that matches destination address
Longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
Examples:
which interface?
which interface?
11001000 00010111 00010110 10100001
200.23.16.0
200.23.23.255
200.23.24.0
200.23.24.255
200.23.31.255
Prefixes in a forwarding table might overlap

## Slide 7: Longest Prefix Matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
Examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
When looking for forwarding table entry for given destination address, use longest address prefix (most specific entry) that matches destination address
Longest prefix match
200.23.16.0
200.23.23.255
200.23.24.0
200.23.24.255
200.23.31.255
Prefixes in a forwarding table might overlap

## Slide 8: Longest Prefix Matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
Examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
When looking for forwarding table entry for given destination address, use longest address prefix (most specific entry) that matches destination address
Longest prefix match
200.23.16.0
200.23.23.255
200.23.24.0
200.23.24.255
200.23.31.255
Prefixes in a forwarding table might overlap

## Slide 9: Longest Prefix Matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
Examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
When looking for forwarding table entry for given destination address, use longest address prefix (most specific entry) that matches destination address
Longest prefix match
200.23.16.0
200.23.23.255
200.23.24.0
200.23.24.255
200.23.31.255
Prefixes in a forwarding table might overlap

## Slide 10: Package Forwarding in a Postal System
Destination prefix | Next hop
UP | Lucknow flight
UP, Prayagraj | Prayagraj flight
West Bengal | Kolkata flight
Maharashtra | Mumbai flight
Postal analogy:
6 packages need to be sent in these addresses
UP, Prayagraj, Barrister Mullah Colony, Swati
UP, Kanpur, Kalyanpur, Amit
West Bengal, Kharagpur, Inda, Manoj
West Bengal, Durgapur, Mahatma Gandhi Rd, Prakash
Maharashtra, Pune, Shivaji Nagar, Vivek
Maharashtra, Nasik, Old Agra Road, Anand
Src: https://pxhere.com/en/photo/1625663

## Slide 11: Longest Prefix Matching
Longest prefix matching: Often performed using ternary content addressable memories (TCAMs)
  Content addressable: Present address to TCAM  retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM
Src: https://www.ciscopress.com/articles/article.asp?p=2264831&seqNum=2

## Slide 12: Host Forwarding
Hosts send the remote traffic to its nearest router
0.0.0.0/0 includes all IP addresses
Prefix | Next hop
My network prefix | Send directly to that destination
0.0.0.0/0 | Send to the router

## Slide 13: How To Obtain IP Address?

## Slide 14: IP Addresses: How to Get One?
That’s actually two questions:
How does a host get IP address within its network (host part of address)?
How does a network get IP address for itself (network part of address)
How does host get IP address?
Hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “Plug-and-play”

## Slide 15: DHCP Client-Server Scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 16: DHCP Client-Server Scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The first two steps can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 17: DHCP: Dynamic Host Configuration Protocol
DHCP overview:
  Host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  Host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 18: DHCP: More Than IP Addresses
DHCP can return more than just allocated IP address on subnet:
  Address of first-hop router for client
  Name and IP address of DNS sever
  Network mask (indicating network versus host portion of address)

## Slide 19: DHCP Example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 20: DHCP Example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
Encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
Router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
Client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 21: How Does Networks Get IP addresses?
Q: How does network get subnet part of IP address?
A: Gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
ISP can then allocate out its address space in 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 22: Hierarchical Addressing: Route Aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Organization 0
Organization 7
Internet
Organization 1
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing information:
ISP-A
ISP-B

## Slide 23: Hierarchical Addressing: More Specific Routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
ISP-A
Organization 0
Organization 7
Internet
200.23.18.0/23
Organization 1
ISP-B
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from ISP-A to ISP-B
ISP-B now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”
200.23.16.0
200.23.19.255
200.23.31.255
200.23.18.0

## Slide 24: Hierarchical Addressing: More Specific Routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Organization 0
Organization 7
Internet
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from ISP-A to ISP-B
ISP-B now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”
ISP-A
ISP-B
200.23.16.0
200.23.19.255
200.23.31.255
200.23.18.0

## Slide 25: How ISPs Get IP Addresses?
ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  Allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  Manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Src: https://commons.wikimedia.org/wiki/File:IPv6_Prefix_Assignment_Example-en.svg
Src: https://commons.wikimedia.org/wiki/File:Regional_Internet_Registries_world_map.svg

## Slide 26: IPv4 Addressing: Concluding Remarks
Are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT helps IPv4 address space exhaustion
IPv6 has 128-bit address space
Src: https://commons.wikimedia.org/wiki/File:IPv4_IANA_and_RIR_exhaustion_time_line-en.svg