## Slide 1: Computer Networks II Network Address Translation and IPv6
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: IPv4 Address Space Exhaustion
IPv4 address space is limited
  Number of Internet users increased exponentially
  NAT: Network Address Translation
  IPv6 addressing
Src: https://commons.wikimedia.org/wiki/File:Internet_Hosts_Count_log.svg
Src: https://commons.wikimedia.org/wiki/File:IPv4_exhaustion_time_line-en.svg

## Slide 3: Network Address Translation

## Slide 4: NAT: Network Address Translation
Local network (e.g., home network)
Rest of
Internet
Home network:
One access point has one IPv4 address
Suppose 10 hosts are connected to the access point
138.76.29.7

## Slide 5: Public and Private IP Address
Local network (e.g., home network)
Rest of
Internet
Private IP address:
Can be reused
10.0.0.0 - 10.255.255.255
172.16.0.0 - 172.31.255.255
192.168.0.0 – 192.168.255.255
138.76.29.7
Public IP address:
Cannot be reused
Globally unique

## Slide 6: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
Local network (e.g., home network) 10.0.0/24
138.76.29.7
Rest of
Internet
Datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
All datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: All devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 7: NAT: Network Address Translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 8: NAT: Network Address Translation
Implementation: NAT router must (transparently):
  Outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  Remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  Incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 9: NAT Traversal Problem
Client wants to connect to server with address 10.0.0.1
  Server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  Only one externally visible NATed address: 138.76.29.7
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 10: NAT Traversal Problem
Solution 1: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  Learn public IP address (138.76.29.7)
  Add/remove port mappings (with lease times)
10.0.0.1, 3345
NAT
router
IGD
Mapping:
10.0.0.1, 3345 to 138.76.29.7, 5001

## Slide 11: NAT Traversal Problem
Solution 2: Relaying (used in Skype)
  NATed client establishes connection to relay
  External client connects to relay
  Relay bridges packets between to connections
138.76.29.7
client
1. connection to
relay initiated
by NATed host
2. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1

## Slide 12: NAT: Network Address Translation
  Advantages:
    Just one IP address needed from provider ISP for all devices
    Can change addresses of host in local network without notifying outside world
    Can change ISP without changing addresses of devices in local network
    Security: devices inside local net not directly addressable, visible by outside world

## Slide 13: NAT: Network Address Translation
NAT has been controversial:
  Routers “should” only process up to layer 3
  Violates end-to-end argument (port # manipulation by network-layer device)
But NAT is here to stay:
  Extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 14: IPv6

## Slide 15: IPv6 Motivation
Initial motivation: 32-bit IPv4 address space would be completely allocated
Additional motivation:
  Speed processing/forwarding: 40-byte fixed length header
  Enable different network-layer treatment of “flows”
IPv6 has a much larger address space (i.e. 128 bits)
Src: https://commons.wikimedia.org/wiki/File:Internet_Hosts_Count_log.svg

## Slide 16: IPv6 Datagram Format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
Important features:
Flow levels for a group of packets
Better fit for advanced features (e.g. mobility, multicasting, security etc.)

## Slide 17: IPv6 Datagram Format
Src: https://www.cisco.com/en/US/technologies/tk648/tk872/technologies_white_paper0900aecd8054d37d.html
Extension headers
  Next header field carries the information of the header following it

## Slide 18: IPv6 Datagram Format
Order | Header Type | Next Header Code
1 | Basic IPv6 Header | -
2 | Hop-by-Hop Options | 0
3 | Destination Options | 60
4 | Routing Header | 43
5 | Fragment Header | 44
6 | Authentication Header | 51
7 | Encapsulation Security Payload Header | 50
8 | Destination Options | 60
9 | Mobility Header | 135
 | No next header | 59
Upper Layer | TCP | 6
Upper Layer | UDP | 17
Upper Layer | ICMPv6 | 58
Src: https://www.cisco.com/en/US/technologies/tk648/tk872/technologies_white_paper0900aecd8054d37d.html

## Slide 19: IPv6 vs IPv4 Header
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
What’s missing (compared with IPv4):
No checksum (to speed processing at routers)
No fragmentation/reassembly
No options (available as upper-layer, next-header protocol at router)
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)

## Slide 20: IPv6 Addressing
IPv6 has a much larger address space (i.e. 128 bits)
  Consists of 8 groups of 4 hex digits (i.e. 16 bits)
Can be written in compact format
  Omit leading zeros
  Omit groups of zeros
Example: 2001:0db8:0000:0000:0000:ff00:0042:b239

## Slide 21: IPv6 Addressing
IPv6 has a much larger address space (i.e. 128 bits)
  Consists of 8 groups of 4 hex digits (i.e. 16 bits)
Can be written in compact format
  Omit leading zeros
  Omit groups of zeros
Example: 2001:0db8:0000:0000:0000:ff00:0000:b239

## Slide 22: IPv6 Addressing
IP addresses have structure:
  Network part: devices in same network have common high order bits
  Host part: remaining low order bits
Example: 2001:0db8:0000:0000:0000:ff00:0000:b239/64

## Slide 23: Transition from IPv4 to IPv6
IPv6 is fundamentally different than IPv4
Not all routers can be upgraded simultaneously
  How will the network operate with mixed IPv4 and IPv6 routers?
Well known approaches:
  Dual stack (supports both IPv4 and IPv6)
  Tunneling (carries IPv6 over IPv4)

## Slide 24: Dual Stack IP Implementation
link
application
transport
Application
Transport
Link
IPv4
IPv6
link
application
transport
Application
Transport
Link
IPv6
link
application
transport
Application
Transport
Link
IPv4
IPv4/IPv6 Host
IPv6 Host
IPv4 Host

## Slide 25: Tunneling and encapsulation
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
Tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  Tunneling used extensively in other contexts (4G/5G)

## Slide 26: Tunneling and Encapsulation
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
IPv4 datagram
IPv6 datagram
Tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 27: Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
Logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!

## Slide 28: IPv6: Adoption
Google: ~40% of clients access services via IPv6 (Sep, 2022)
NIST: 1/3 of all US government domains are IPv6 capable
Src: https://www.google.com/intl/en/ipv6/statistics.html#tab=ipv6-adoption

## Slide 29: Summary
Network Address Translation:
  Helps IPv4 address space exhaustion
IPv6 Addressing:
  IPv6 datagram format
  Tunnelling and Encapsulation