## Slide 1: Computer Networks II Internet Control Message Protocol (ICMP)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: ICMP: Internet Control Message Protocol
Used by hosts and routers to communicate network-level information
  Error reporting: unreachable host, network, port, protocol
  Diagnostic purposes: echo request/reply (used by ping)
Src: https://study-ccna.com/icmp-internet-control-message-protocol/

## Slide 3: ICMP: Internet Control Message Protocol
ICMP message: Type, code, checksum
  In case of error message it also contains the IP header + first 8 bytes of IP datagram causing error
    Sender of the IP datagram can infer the problem
Type Code Description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 dest port unreachable
3 4 fragmentation required, DF set
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
Src: https://commons.wikimedia.org/wiki/File:ICMP_header_-_General-en.svg

## Slide 4: ICMP: Internet Control Message Protocol
ICMP messages carried in IP datagrams
  Protocol number = 1
Src: https://commons.wikimedia.org/wiki/File:ICMPv4_encapsulation-en.svg
Src: https://commons.wikimedia.org/wiki/File:ICMP_header_-_General-en.svg

## Slide 5: IP Datagram Format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 6: MTU Discovery and ICMP
Fragmentation is often undesirable
More overhead for the routers
Solution: discover the MTU that will fit for all the links
  Implemented using ICMP (type 3, code 4)  DF bit is set to 1
Src: https://www.cisco.com/c/en/us/support/docs/ip/generic-routing-encapsulation-gre/25885-pmtud-ipfrag.html

## Slide 7: Traceroute and ICMP
When ICMP message arrives at source: record RTTs
Stopping criteria:
UDP segment eventually arrives at destination host
Destination returns ICMP “port unreachable” message (type 3, code 3)
Source stops
3 probes
3 probes
3 probes
Source sends sets of UDP segments to destination
  1st set has TTL =1, 2nd set has TTL=2, etc.
  Destination port is set to an unlikely number
Datagram in n-th set arrives to n-th router:
  Router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 8: Summary
Internet Control Message Protocol:
  ICMP message format
  MTU discovery and ICMP
  Traceroute and ICMP