## Slide 1: Computer Networks II Routing Algorithms Link State Routing
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Routing Protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
Path: Sequence of routers packets traverse from given initial source host to final destination host
“Good”: least “cost”, “fastest”, “least congested”, “shortest”
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 3: Routing Algorithm Classification
Global (centralized): All routers have complete topology, link cost info
“Link state” algorithms
Decentralized: iterative process of computation, exchange of info with neighbors
Routers initially only know link costs to attached neighbors
“Distance vector” algorithms
How fast do routes change?
Dynamic: routes change more quickly
  periodic updates or in response to link cost changes
Static: routes change slowly over time
Global or decentralized information?

## Slide 4: Link State Routing Protocol

## Slide 5: Graph Abstraction: Link Costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 6: Link-state Routing Algorithm
Runs in two steps
Step1: Learning the network topology
  Nodes flood the information about their neighbors and their link costs in Link State Packets
  All nodes learn the entire network topology
Step2: Finding the shortest path
  Each node runs Dijkstra’s algorithm to find out the shortest path (or least cost path) corresponding to each destination

## Slide 7: Learning the Network Topology
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
LS packet for u
v
x
w
2
1
5
Neighbor
Cost
LS packet for v
u
x
w
2
2
3
Neighbor
Cost
LS packet for w
u
v
x
y
z
5
3
3
1
5
Neighbor
Cost
LS packet for x
u
v
w
y
1
2
3
1
Neighbor
Cost
LS packet for y
w
x
z
1
1
2
Neighbor
Cost
LS packet for z
w
y
5
2
Neighbor
Cost

## Slide 8: Dijkstra’s Link-state Routing Algorithm
Centralized: network topology, link costs known to all nodes
Computes least cost paths from one node (“source”) to all other nodes
  Gives forwarding table for that node
Iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
Notation

## Slide 9: Dijkstra’s Link-state Routing Algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes a
4 if a adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(a) = cu,a /* but may not be minimum cost */
6 else D(a) = ∞
7 Loop
8
9
10
11
12
13 until all nodes in N'
find a not in N' such that D(a) is minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
/* new least-path-cost to b is either old least-cost-path to b or known least-cost-path to a plus direct-cost from a to b */
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
Notation

## Slide 10: Dijkstra’s Algorithm: An Example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
4,y
D(w),p(w)
4,y
3,y
5,u
∞
∞
1,u
2,u
∞
2,x
4,x
2,u
4,y
3,y
2,u
uxyvwz
uxyvw
uxyv
uxy
ux
u
v
w
x
y
z
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to u, then D(a) = cu,a
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
Notation

## Slide 11: Dijkstra’s Algorithm: An Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
y
x
w
v
z
Resulting least-cost-path tree from u:
Resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
Destination
Outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 12: Dijkstra’s Algorithm: Another Example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
1
2
3
4
5
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
uwxvyz
v
w
x
y
z

## Slide 13: Dijkstra’s Algorithm: Discussion
Algorithm complexity: n nodes
Each of n iteration: need to check all nodes, a, not in N'
n(n+1)/2 comparisons: O(n2) complexity
More efficient implementations possible: O(nlogn)
Memory requirement: If each nodes has k neighbors  memory required to store the link states is O(nk)
Message complexity:
Each router must broadcast its link state information to other n routers
Efficient broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
Each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 14: Handling Failures
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
LS packet for u
v
x
w

1
5
Neighbor
Cost
LS packet for v
u
x
w

2
3
Neighbor
Cost
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
LS packet for x
u
v
w
y

2
3
1
Neighbor
Cost
LS packet for v
u
x
w

2
3
Neighbor
Cost
LS packet for w
u
v
x
y
z

3
3
1
5
Neighbor
Cost
Link failure
Node failure

## Slide 15: Dijkstra’s Algorithm: Oscillations
When link costs depend on traffic volume, route oscillations possible
a
d
c
b
1
1+e
e
0
e
1
1
0
0
Initially
a
d
c
b
Given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
a
d
c
b
Given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
a
d
c
b
Given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
Sample scenario:
  Routing to destination a, traffic entering at b, c, d with rates 1, e (<1), 1
  Link costs are directional, and volume-dependent
e
1
1
e
1
1
e
1
1

## Slide 16: Summary
Routing algorithms:
  Centralized vs decentralized
  Static vs dynamic
Link state routing algorithm:
  Limitations: may lead to oscillations