## Slide 1: Computer Networks Intra-AS Routing RIP and OSPF
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Making Routing Scalable
Routing studied thus far - idealized
All routers identical
Network “flat”
This is not true in practice
Scale: billions of destinations:
Can’t store all destinations in routing tables
Routing table exchange would swamp links
Administrative autonomy:
Internet: a network of networks
Each network admin may want to control routing in its own network
Tier1 ISP
Tier1 ISP
Tier1 ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
…
…
…
…
Tier3
ISP
Tier3
ISP
Tier2 ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier2 ISP
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3

## Slide 3: Internet Approach to Scalable Routing
Autonomous systems (AS) (a.k.a. “domains”): group of routers controlled by a single administrative entity, i.e. an ISP, a company, a university
Intra-AS (aka “intra-domain”): routing within an AS (“network”)
All routers in AS must run same intra-domain protocol
Routers in different AS can run different intra-domain routing protocols
Gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
Also called Interior Gateway Protocol
Inter-AS (aka “inter-domain”): routing among AS’es
Gateways perform inter-domain routing (as well as intra-domain routing)
Also called Exterior Gateway Protocol

## Slide 4: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
Inter-AS routing
Forwarding
table
Forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  Intra-AS routing determine entries for destinations within AS
  Inter-AS & intra-AS determine entries for external destinations

## Slide 5: Inter-AS Routing: A Role in Intra-domain Forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
Suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
Learn which destinations reachable through AS2, which through AS3
Propagate this reachability info to all routers in AS1
  Router should forward packet to gateway router in AS1, but which one?

## Slide 6: Intra-AS Routing: Routing within an AS
Most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  Classic DV
  No longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  Formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  Link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 7: Routing Information Protocol

## Slide 8: RIP ( Routing Information Protocol)
Included in BSD-UNIX distribution in 1982
Distance vector algorithm
  Distance metric: # hops (max = 15 hops), each link has cost 1
    Hop: number of subnets traversed along the shortest path from source router to destination subnet
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  Each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
Subnet Hops
u 1
v 2
w 2
x 3
y 3
z 2
From router A to destination subnets:

## Slide 9
w
x
y
z
A
C
D
B
Destination subnet Next-router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
Routing table in router D
A
5
Dest Next-router #hops
w - 1
x - 1
z C 4
A-to-D advertisement
RIP (Routing Information Protocol)

## Slide 10: RIP: Link Failure and Recovery
If no advertisement heard after 180 sec  neighbor/link declared dead
  Routes via neighbor invalidated
  New advertisements sent to neighbors
  Neighbors in turn send out new advertisements (if tables changed)
  Link failure info quickly propagates to entire net
  Poisoned reverse used to prevent ping-pong loops (infinite distance = 16 hops)

## Slide 11: OSPF (Open Shortest Path First) Routing

## Slide 12: OSPF (Open Shortest Path First) Routing
“Open”: Publicly available
Classic link-state
  Each router floods OSPF link-state advertisements to all other routers in entire AS
  Multiple link costs metrics possible: bandwidth, delay
  Each router has full topology, uses Dijkstra’s algorithm to compute forwarding table

## Slide 13: OSPF : Advanced Features
Security: All OSPF messages can be authenticated (to prevent malicious intrusion)
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different ToS
  Satellite link cost set low for best effort ToS; high for real-time ToS
Integrated unicast and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains

## Slide 14: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements flooded only in area, or backbone
  Each node has detailed area topology; only knows direction to reach other destinations
Area border routers: “summarize” distances to destinations in own area, advertise in backbone
Area 1
Area 2
Area 3
Backbone
Internal
routers
Backbone router: runs OSPF limited to backbone
Boundary router: connects to other ASes
Local routers:
Flood LS in area only
Compute routing within area
Forward packets to outside via area border router

## Slide 15: Summary
Internet Approach to Scalable Routing:
  Intra-AS and Inter-AS
Intra-AS routing:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First