## Slide 1: Computer Networks Inter-AS Routing Border Gateway Protocol (BGP)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Inter-AS and Intra-AS Routing
Tier1 ISP
Tier1 ISP
Tier1 ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
…
…
…
…
Tier3
ISP
Tier3
ISP
Tier2 ISP
Tier3
ISP
Tier3
ISP
Tier3
ISP
Tier2 ISP
AS: controlled by a single administrative entity, i.e. an ISP
Src:https://commons.wikimedia.org/wiki/File:India_and_Neighbouring_Countries_Map_(official_borders).png

## Slide 3: Inter-AS Routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “Glue that holds the Internet together”
Allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet
Relations among the ASes depend on multiple factors  competitions, politics, economy etc.
  Transmit: One AS pays another one for access to the Internet
  Peer: Two ASes exchange traffic between their users freely, and for mutual benefit
Src: https://fr.wikipedia.org/wiki/Peering#/media/Fichier:AS-interconnection.svg

## Slide 4: Inter-AS Routing: BGP
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  Determine “good” routes to other networks based on reachability information and policy
eBGP connectivity
Logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
Gateway routers run both eBGP and iBGP protocols

## Slide 5: BGP and Policy Based Path Advertisement

## Slide 6: BGP Path Advertisement
When AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection (port 179):
  Advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
  BGP sessions do not correspond to physical links
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 7: BGP Path Advertisement
Route advertisement contain an IP prefix + attributes
  Prefix: destination being advertised
  Two important attributes:
    AS-PATH: list of ASes through which prefix advertisement has passed (AS50, AS76)
    NEXT-HOP: indicates the router interface that begins the AS-PATH
    The intra-AS routing protocol will determine the least-cost paths to all subnets attached to the routers in the AS, including the subnet for the link between CE1 and PE-1
Src: http://bgphelp.com/2017/03/05/bgp-next-hop-self-explained/

## Slide 8: BGP Path Advertisement
Policy-based advertisement:
  Import policy: Gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  Export policy: AS policy also determines whether to advertise path to other other neighboring ASes
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
BGP advertisement:
AS3, X

## Slide 9: BGP Path Advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers  import policy
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c  export policy
AS3, X

## Slide 10: BGP: Achieving Policy via Advertisements
B
Legend:
Customer
network:
Provider
network
A advertises path Aw to B and to C
B chooses not to advertise BAw to C
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks

## Slide 11: BGP: Achieving Policy via Advertisements
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
Policy to enforce: x does not want to route from B to C via x
  So x will not advertise to B a route to C
B
Legend:
Customer
network:
Provider
network
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks

## Slide 12: BGP and Policy Based Routing

## Slide 13: BGP Route Selection
Router may learn about more than one route to destination AS, selects route based on:
  Local preference value attribute: policy decision
    Set by the import policy
  Shortest AS-PATH
    Included in the route advertisement
  Closest NEXT-HOP router: Hot potato routing
    Based on intra-domain routing protocol (i.e. OSPF)
  Additional criteria (like smallest NEXT-HOP router id etc.)
2b
2d
2c
2a
AS 2
AS4,AS5,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 14: BGP Route Selection
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
Gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 15: BGP Route Selection
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
At 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
Dest
Interface
…
…
…
…
At 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 16: BGP Route Selection
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
At 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
At 1d: to get to X, use interface 1
Dest
Interface
…
…
…
…
1c
2
X
2
At 1a: OSPF intra-domain routing: to get to 1c, use interface 2
At 1a: to get to X, use interface 2

## Slide 17: BGP Messages
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
Src: https://onlinelibrary.wiley.com/doi/10.1002/dac.5266?af=R
BGP messages exchanged between peers over TCP connection

## Slide 18: Inter-AS vs Intra-AS Routing
Inter-AS: admin wants control over how its traffic routed, who routes through its network
  Policy dominates over performance
Intra-AS: single admin, so policy less of an issue  can focus on performance