## Slide 1: Computer Networks Transport Layer - Introduction
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur
Application
Transport
Network
Link
Physical

## Slide 2: Transport Layer Services and Protocols
Provide logical communication between application processes running on different hosts
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
Transport protocols actions in end systems:
  Sender: breaks application messages into segments, passes to network layer
  Receiver: reassembles segments into messages, passes to application layer
Two transport protocols available to Internet applications
  TCP, UDP
Notes: By logical communication , we
mean that from an application’s perspective, it is as if the hosts running the processes
were directly connected; in reality, the hosts may be on opposite sides of the
planet, connected via numerous routers and a wide range of link types. Application
processes use the logical communication provided by the transport layer to send
messages to each other, free from the worry of the details of the physical infrastructure
used to carry these messages.
Let’s look at each of these three (logical communications, actions,

## Slide 3: Transport vs Network Layer Services
Network layer: host-to-host delivery
Transport layer: logical communication between processes
  relies on, enhances, network layer services
Src: https://commons.wikimedia.org/wiki/File:IP_stack_connections_(corrected).svg

## Slide 4: Sockets
Socket: door between application process and end-end-transport protocol
  An application process can send/receive messages to/from another application process via a socket
Internet
controlled
by OS
controlled by
app developer
Transport
Application
Physical
Link
Network
process
Transport
Application
Physical
Link
Network
process
Socket

## Slide 5: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg

## Slide 6: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
transport
Receiver:
app. msg
extracts application-layer message
checks header values
receives segment from IP
Th
app. msg
demultiplexes message up to application via socket

## Slide 7: Two Principal Internet Transport Protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  reliable, in-order delivery
  congestion control
  flow control
  connection setup
UDP: User Datagram Protocol
  unreliable, unordered delivery
  no-frills extension of “best-effort” IP

## Slide 8: Multiplexing and Demultiplexing

## Slide 9: Multiplexing/demultiplexing
Process
Socket
Use header info to deliver
received segments to correct
socket
Demultiplexing at receiver:
Handle data from multiple
sockets, add transport header (later used for demultiplexing)
Multiplexing at sender:
Transport
Application
Physical
Link
Network
P2
P1
Transport
Application
Physical
Link
Network
P4
Transport
Application
Physical
Link
Network
P3

## Slide 10: How Demultiplexing Works
Host receives IP datagrams
  Each datagram has source IP address, destination IP address
  Each datagram carries one transport-layer segment
  Each segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate socket
Source port #
Dest port #
Application data
Other header fields
TCP/UDP segment format
Src: https://linuxwheel.com/chapter-5-fundamentals-of-tcp-ip-transport-and-application/

## Slide 11: Connectionless Demultiplexing
When host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
When creating datagram to send into UDP socket, must specify
  Destination IP address
  Destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 12: Connectionless Demultiplexing
DatagramSocket serverSocket = new DatagramSocket (6428)
Transport
Application
Physical
Link
Network
P3
Transport
Application
Physical
Link
Network
P1
Transport
Application
Physical
Link
Network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775)
DatagramSocket mySocket2 = new DatagramSocket (9157)
Source port: 9157
Dest port: 6428
Source port: 6428
Dest port: 9157
Source port: 6428
Dest port: 5775
Source port: 5775
Dest port: 6428

## Slide 13: Connection-Oriented Demultiplexing
TCP socket identified by 4-tuple:
  Source IP address
  Source port number
  Dest IP address
  Dest port number
Demux: receiver uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  Each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client

## Slide 14: Connection-Oriented Demultiplexing
Transport
Application
Physical
Link
Network
P3
Transport
Application
Physical
Link
P4
Transport
Application
Physical
Link
Network
P2
source IP,port: A,9157
dest IP, port: B,80
Host: IP address A
Host: IP address C
Network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
Server: IP address B

## Slide 15: Summary
Transport layer protocols:
  Multiplexing, demultiplexing
UDP: Demultiplexing using destination IP address and port number
TCP: Demultiplexing using 4-tuple: source and destination IP addresses, and port numbers