## Slide 1: Computer Networks II User Datagram Protocol
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: UDP: User Datagram Protocol
“No frills,” “bare bones” Internet transport protocol
“Best effort” service, UDP segments may be:
  Lost, duplicated
  Delivered out-of-order to app
Connectionless:
  No handshaking between UDP sender, receiver
  Each UDP segment handled independently of others
Src: https://commons.wikimedia.org/wiki/File:Fig2_UDPwork.jpg

## Slide 3: UDP: User Datagram Protocol
UDP use:
  Streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  DHCP
  HTTP/3
If reliable transfer needed over UDP (e.g., HTTP/3):
  Add needed reliability at application layer
  Add congestion control at application layer
No connection establishment (which can add RTT delay)
Simple: no connection state at sender, receiver
Small header size
No congestion control
  UDP can blast away as fast as desired!
Why is there a UDP?

## Slide 4: UDP Segment Header
source port #
dest port #
32 bits
application
data
(payload)
length
checksum
length, in bytes of UDP segment, including header
data to/from application layer
Checksum covers UDP segment + IP pseudoheader
  Optional in IPv4, compulsory in IPv6
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
UDP segment format
IPv6 datagram format
IPv4 datagram format
Info: https://www.packetmania.net/en/2021/12/26/IPv4-IPv6-checksum/

## Slide 5: UDP Checksum
Suppose a segment consists of these bits:
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
sum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
Transmitted bits:

## Slide 6: UDP checksum
Sender:
Treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
Checksum: addition (one’s complement sum) of segment content
Checksum value put into UDP checksum field
Receiver:
Compute the addition of the segment contents including the checksum
Check if computed sum equals to all 1’s:
  Not all 1’s - error detected
  All 1’s - no error detected. But maybe errors nonetheless?
Goal: Detect errors (i.e., flipped bits) in transmitted segment

## Slide 7
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
sum
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!
UDP Checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
Suppose a segment consists of these bits:

## Slide 8: Summary: UDP
“No frills” protocol:
  Segments may be lost, delivered out of order
  Best effort service: “send and hope for the best”
UDP has its plusses:
  No setup/handshaking needed (no RTT incurred)
  Helps with reliability (checksum)
Build additional functionality on top of UDP in application layer (e.g., HTTP/3)