## Slide 1: Computer Networks Transmission Media (Unguided) and Antennas
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Antennas
Electrical conductors used to radiate or collect electromagnetic energy
Transmission antenna: Electrical energy  converted to electromagnetic energy  radiated into the surrounding
Reception antenna: Electromagnetic energy  converted to electrical energy  fed to the receiver

## Slide 3: Isotropic Antennas
Isotropic antenna:
  A point in space that radiates power in all directions equally with a spherical radiation pattern
Src: https://en.wikipedia.org/wiki/Free-space_path_loss

## Slide 4: Isotropic Antennas

## Slide 5: Omni-directional Antennas
Omni-directional antenna: power propagates uniformly in all directions in a plane
  Cell phones, FM radios, walkie-talkies etc.
Src: https://commons.wikimedia.org/wiki/File:Elem-doub-rad-pat-pers.svg

## Slide 6: Directional Antennas
Directional antenna: Parabolic reflective antenna

## Slide 7: Antennas
Directional antenna: Parabolic reflective antenna
  Satellite communications, radio telescopes etc.
Src:https://commons.wikimedia.org/wiki/File:Antenna_03.JPG

## Slide 8: Antenna Gain
Antenna gain:
  Measure of directionality
  Defined as the power output in a particular direction, compared to that produced in any direction by a perfect isotropic antenna (dBi)
  http://www.cisco.com/en/US/prod/collateral/wireless/ps7183/ps469/product_data_sheet09186a008008883b.html
Radiated power of directional antenna
Radiated power of isotropic antenna
Src: https://www.ahsystems.com/articles/Understanding-antenna-gain-beamwidth-directivity.php

## Slide 9: Antenna Gain
Consider a directional antenna with a gain of 6 dB over a reference antenna and that radiates 700 W. How much power must the reference antenna radiates to provide the same signal power in the preferred direction?
Src: https://www.ahsystems.com/articles/Understanding-antenna-gain-beamwidth-directivity.php

## Slide 10: Antenna Gain
Antenna gain:
  Relates to the effective area of the antenna
  Effective area of an antenna is related to its physical size and its shape
  Effective area of an ideal isotropic antenna is , with a power gain = 1
=

## Slide 11: Antenna Gain
Antenna gain:
  Relates to the effective area of the antenna
  Effective area of an antenna is related to its physical size and its shape
  Effective area of an parabolic antenna with a face area of A is , with a power gain of
=

## Slide 12: Antenna Gain
For a parabolic reflective antenna with a diameter of 2 m, operating at 12 GHz, what is the effective area and the antenna gain?
=

## Slide 13: Free Space Path Loss
Free space path loss:
: Transmit antenna gain
: Receiver antenna gain
  Receiver antenna provides an aperture with an effective area for receiving a fraction of the transmitted power

## Slide 14: Free Space Path Loss
Assume that a ground station is transmitting a signal of 250 W to a satellite at 4 GHz (earth to satellite distance is 35863 km). The antenna gains are 44 dB and 48 dB. What is the received power?

## Slide 15: Summary
Wireless transmission medium:
  Isotropic, omnidirectional and directional antenna
  Free space path loss
  Antenna gain