## Slide 1: Computer Networks I Some Performance Metrics
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Throughput
Throughput: Rate (bits/time unit) at which bits are being sent from sender to receiver
  Instantaneous: Rate at given point in time
  Average: Rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 3: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 4: Related Terminologies/Metrics
Datarate/Bitrate: Rate (bits/time unit) at which bits are being sent/received at the physical layer
Throughput: Rate (bits/time unit) at the network layer to measure the end-to-end performance

## Slide 5: Related Terminologies/Metrics
Throughput: Rate (bits/time unit) at the network layer to measure the end-to-end performance
  A related terminology that used is goodput
Difference between throughput and goodput:
  Throughput: Number of bits received per unit time
  Goodput: Number of useful bits received per unit time
Data
Header
9000 bits
1000 bits
Suppose we are sending 1 pkts/sec
Throughput: 10000 bps
Goodput: 9000 bps

## Slide 6: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Delay/Latency: Time taken by the packet to reach the destination

## Slide 7: Packet delay: four sources
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d /s
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Delay/Latency: Time taken by the packet to reach the destination

## Slide 8: Packet delay: four sources
dproc
dtrans
dqueue
dtrans
dproc
dprop
Cross traffic

## Slide 9: Round Trip Time (RTT)
RTT = 2 Propagation time
RTT
Client
Server

## Slide 10: Transmission and Propagation Delay
Consider a scenario where the distance between the transmitter and receiver is 12000 km, and the signal travels through the transmission link (connecting the transmitter-receiver) is 2108 m/s. Also assume that the transmitter is transmitting a 2 KB of message, and the link transmission rate is 1 Mbps. Find out the transmission and propagation delay.

## Slide 11: Transmission and Propagation Delay
Consider a scenario where the distance between the transmitter and receiver is 12000 km, and the signal travels through the transmission link (connecting the transmitter-receiver) is 2108 m/s. Also assume that the transmitter is transmitting a 5 MB of message, and the link transmission rate is 1 Gbps. Find out the transmission and propagation delay.

## Slide 12: Packet queueing delay
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R  1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 13: How do packet delay and loss occur?
Packets queue in router buffers, waiting for turn for transmission
  Queue length grows when arrival rate to link (temporarily) exceeds output link capacity
Packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted
buffer
(waiting area)
packet arriving to
full buffer is lost

## Slide 14: Bandwidth-Delay Product
Bandwidth-delay product:
  Think about the link between two points as a pipe
  The cross section of the pipe represents the bandwidth
  The length of the pipe represents the delay
We can say the volume of the pipe defines the bandwidth-delay product

## Slide 15: Bandwidth-Delay Product
Bandwidth-delay product: Number of bits which can be transmitted before an ACK is received from the receiver
  The number of bits that can be transmitted before you know that something is wrong
  Estimation of number of bits “in transit” through the transmission medium

## Slide 16: Bandwidth-Delay Product
Moderate speed satellite network: 512 kbit/s, 900 ms RTT
Residential DSL: 2 Mbit/s, 50 ms RTT
High speed LAN: 100 Gbit/s, 30 s RTT

## Slide 17: Jitter
Jitter is a measure of packet delay variance
  Happens when different packets of data face different delays in a network
  Important for time-sensitive receiver applications, i.e. audio or video
Example: If the delay of the 1st, 2nd, and 3rd packets are 10ms, 25 ms and 50 ms respectively  real-time application experiences jitter

## Slide 18: Jitter
Jitter is negative and causes network congestion and packet loss
  Leads to flickering of a display screen
  Introduces clicks or other undesired impacts in audio signals

## Slide 19: Summary
Useful performance metrics:
  Datarate vs Throughput vs Goodput
  Delay
  Delay-bandwidth product
  Jitter